## Slide 1: Manifold meta-learning for reduced-complexity neural system identification
Marco Forgione, Ankush Chakrabarty, Dario Piga, Matteo Rufolo, Alberto Bemporad

## Slide 2: Motivation
Neural network models can effectively describe a wide variety of dynamical systems
However, they are often overparameterized. Training is computationally expensive and data-hungry.
We aim at discovering a manifold where the parameters lie for a class of systems
Given the manifold, we can learn a new system with little data and compute

## Slide 3: Motivation
Physics-based modeling
Bergman model of glucose-insulin metabolism
, physical coefficients
Black-box modeling
Generic neural state-space model
containts black-box parameters.
learned parameter manifold.
The usual story is: let’s embed some physics in the black-box model
Here, we instead seek a low-dimensional manifold in the black-box parameter space
How small can be?

## Slide 4: Motivation
Physics-based modeling
Two-tank system
, physical coefficients
Black-box modeling
Generic neural state-space model
containts black-box parameters.
learned parameter manifold.
The usual story is: let’s embed some physics in the black-box model
Here, we instead seek a low-dimensional manifold in the black-box parameter space
How small can be?

## Slide 5: Framework
We are given:
A meta-dataset, namely a dataset of related of datasets: Could be simulations with randomized physical parameters or historical datasets.
A base architecture (neural network)
Each dataset is well described by (at least) one unknown . We may fit models solving:
The architecture is over-parameterized, i.e. has more degrees of freedom (weights) than the intrinsic factors of variation across datasets (physical parameters). Fitting the model may be heavy and generalization poor.

## Slide 6: Framework
Each may be seen as a sample from a distribution .
The dataset distribution is characterized by:
Random input sequences
A small latent which specifies the dependency
Latent is the subset of physical parameters that vary across datasets. Fixed ones are part of
Example:
Robot where only the payload changes across experiments
Curation process where some ingredients are fixed (?)
…
This further motivates the search of a manifold in the neural network’s parameter space

## Slide 7: Objective
Learn a manifold such that the base architecture restricted to the manifold:
retains the capacity to represent each in the meta-dataset for some
Then, use it for reduced-order modeling. Given new data , solve: This should work well if comes from !

## Slide 8: Methodology
We parameterize the manifold function with a vector :
We split each dataset in train and test portions:
In principle, the best could be the result of a bi-level optimization: where

## Slide 9: Methodology
For simplicity, we replace the inner optimization with an auxiliary neural network
We approximate the expected value with samples from and minimize wrt with minibatch gradient descent

## Slide 10: Results
Experiments on the Bouc-Wen system identification benchmark (hysteretic oscillator).
: MLPs with 1 hidden layers, 16 units ()
Training on 40960 points leads an almost perfect model
Can we learn with less data?
Base architecture
System dynamics
Test fit: 98.9%

## Slide 11: Results
We learn a reduced-order architecture with free parameters over a meta dataset generated by random systems with parameters in the min-max range
We then fit reduced-order models to sequences of increasing length 100, 200, …, 5000
Reduced-order training is way more data- and compute-efficient

## Slide 12: Conclusions and future works
Meta-learning of a reduced architecture as a manifold in the parameter space
Experiments on a common system identification benchmark
Increased data- and compute-efficiency
Future developments:
Variational setting to learn a reduced-order prior over the manifold
Combination with physics-inspired modeling
Extensions to state estimation and control

## Slide 13: Results
Training of the base architecture:
Interestingly, the Hessian of the loss at the optimum
is close to degenerate in many directions. This further motivates reduced-order architectures
Test fit: 98.9%

## Slide 14: Methodology
In principle, the best could be the result of a bi-level optimization:
We replace the inner optimization with an auxiliary network